LIST PROGRAM ROBOT PEMBAWA  BARANG KENDALI OTOMATIS DAN MANUAL

#include <LiquidCrystal.h>

#include <Servo.h>

LiquidCrystal lcd(8, 9, 10, 11, 12, 13);

#include <PS2X_lib.h>

#define PS2_DAT        4

#define PS2_CMD      6

#define PS2_SEL        5

#define PS2_CLK        7

#define pressures   false

#define rumble      false

PS2X ps2x; // create PS2 Controller Class

int error = 0;

byte type = 0;

byte vibrate = 0;

byte barang = 0;

byte benda = 0;

int sw1 = 23;

int sw2 = 25;

int sw3 = 24;

int sw4 = 22;

int sensorValue1 = 0;  // variable to store the value coming from the sensor

int sensorValue2 = 0;

int sensorValue3 = 0;

int sensorValue4 = 0;

int sensorValue5 = 0;

int tresh = 400;

int timer = 200;

int sharpPin = A5;

int sharp = 0;

int sensorPin1 = A0;    // select the input pin for the potentiometer

int sensorPin2 = A1;

int sensorPin3 = A2;

int sensorPin4 = A3;

int sensorPin5 = A4;

#define pwm_ka 2

#define pwm_ki 3

int m_ka = 26;

int m_ki = 27;

Servo grip_ka, grip_ki, grip_te, grip_ba;

byte ka, ki, te, ba;

int redPin = A9;

int red = 0;

int redaPin = A10;

int reda = 0;

void setup() {

lcd.begin(16, 2);

//..............ps2..........//

Serial.begin(115200);

delay(300);

error = ps2x.config_gamepad(PS2_CLK, PS2_CMD, PS2_SEL, PS2_DAT, pressures, rumble);

if (error == 0) {

Serial.print("Found Controller, configured successful ");

Serial.print("pressures = ");

if (pressures)

Serial.println("true ");

else

Serial.println("false");

Serial.print("rumble = ");

if (rumble)

Serial.println("true)");

else

{ Serial.println("false");

Serial.println("Try out all the buttons, X will vibrate the controller, faster as you press harder;");

Serial.println("holding L1 or R1 will print out the analog stick values.");

Serial.println("Note: Go to www.billporter.info for updates and to report bugs.");

lcd.setCursor(0, 0);

lcd.print("bismillah");

}

}

else if (error == 1)

Serial.println("No controller found, check wiring, see readme.txt to enable debug. visit www.billporter.info for troubleshooting tips");

else if (error == 2)

Serial.println("Controller found but not accepting commands. see readme.txt to enable debug. Visit www.billporter.info for troubleshooting tips");

else if (error == 3)

Serial.println("Controller refusing to enter Pressures mode, may not support it. ");

//  Serial.print(ps2x.Analog(1), HEX);

type = ps2x.readType();

switch (type) {

case 0:

Serial.print("Unknown Controller type found ");

break;

case 1:

{

Serial.print("DualShock Controller found ");

}

break;

case 2:

Serial.print("GuitarHero Controller found ");

break;

case 3:

Serial.print("Wireless Sony DualShock Controller found ");

break;

}

//..........................//

//..........pin............//

pinMode(sw1, INPUT_PULLUP);

pinMode(sw2, INPUT_PULLUP);

pinMode(sw3, INPUT_PULLUP);

pinMode(sw4, INPUT_PULLUP);

pinMode(m_ka, OUTPUT);

pinMode(m_ki, OUTPUT);

digitalWrite(m_ka, LOW);

digitalWrite(m_ki, LOW);

pwm(255, 255);

grip_ka.attach(A8);

grip_ki.attach(A7);

grip_te.attach(A6);

grip_ba.attach(A9);

awal();

//......................//

}

void loop() {

int sensorVal = digitalRead(sw1);

int sensorVal1 = digitalRead(sw2);

int sensorVal2 = digitalRead(sw3);

lcd.setCursor(0, 1);

lcd.print("Allahuakbar");

pwm(255, 255);

awal();

if (sensorVal == LOW) {

lcd.clear();

hidup();

}

if (sensorVal1 == LOW) {

lcd.clear();

hidup1();

}

if (sensorVal2 == LOW) {

lcd.clear();

hidup2();

}

}

void hidup() {

while (1)

{

int sensorVal3 = digitalRead(sw4);

lcd.setCursor(0, 0);

lcd.print("ceksensor");

ceksensor();

if (sensorVal3 == LOW) {

lcd.clear();

break;

}

}

return;

}

void hidup1() {

while (1)

{

int sensorVal3 = digitalRead(sw4);

lcd.setCursor(0, 0);

lcd.print("Otomatis");

otomatis();

if (sensorVal3 == LOW) {

lcd.clear();

break;

}

}

return;

}

void hidup2() {

while (1)

{

int sensorVal3 = digitalRead(sw4);

lcd.setCursor(0, 0);

lcd.print("Manual");

manual();

if (sensorVal3 == LOW) {

lcd.clear();

break;

}

}

return;

}

//***************ceksensor*****************************//

void ceksensor() {

sensorValue1 = analogRead(sensorPin1);

sensorValue2 = analogRead(sensorPin2);

sensorValue3 = analogRead(sensorPin3);

sensorValue4 = analogRead(sensorPin4);

sensorValue5 = analogRead(sensorPin5);

sharp = analogRead(sharpPin);

if (sharp >= 350)

{

lcd.setCursor(8, 1);

lcd.print("GP=1");

}

else {

lcd.setCursor(8, 1);

lcd.print("GP=0");

}

if (sensorValue1 >= tresh)

{

lcd.setCursor(0, 1);

lcd.print("1");

delay(timer);

}

if (sensorValue2 >= tresh)

{

lcd.setCursor(1, 1);

lcd.print("1");

delay(timer);

}

if (sensorValue3 >= tresh)

{

lcd.setCursor(2, 1);

lcd.print("1");

delay(timer);

}

if (sensorValue4 >= tresh)

{

lcd.setCursor(3, 1);

lcd.print("1");

delay(timer);

}

if (sensorValue5 >= tresh)

{

lcd.setCursor(4, 1);

lcd.print("1");

delay(timer);

}

if (sensorValue1 < tresh) {

lcd.setCursor(0, 1);

lcd.print("0");

delay(timer);

}

if (sensorValue2 < tresh) {

lcd.setCursor(1, 1);

lcd.print("0");

delay(timer);

}

if (sensorValue3 < tresh) {

lcd.setCursor(2, 1);

lcd.print("0");

delay(timer);

}

if (sensorValue4 < tresh) {

lcd.setCursor(3, 1);

lcd.print("0");

delay(timer);

}

if (sensorValue5 < tresh) {

lcd.setCursor(4, 1);

lcd.print("0");

delay(timer);

}

}

//****************navigasi motor dc***************//

void maju() {

digitalWrite(m_ka, LOW);

digitalWrite(m_ki, LOW);

}

void kanan() {

digitalWrite(m_ka, HIGH);

digitalWrite(m_ki, LOW);

}

void kiri() {

digitalWrite(m_ka, LOW);

digitalWrite(m_ki, HIGH);

}

void mundur() {

digitalWrite(m_ka, HIGH);

digitalWrite(m_ki, HIGH);

}

//***********************************************//

//****************baca garis*********************//

void jalan() {

sensorValue1 = analogRead(sensorPin1);

sensorValue2 = analogRead(sensorPin2);

sensorValue3 = analogRead(sensorPin3);

sensorValue4 = analogRead(sensorPin4);

sensorValue5 = analogRead(sensorPin5);

if (sensorValue1 < tresh && sensorValue2 >= tresh && sensorValue3 >= tresh && sensorValue4 >= tresh && sensorValue5 < tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 >= tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 < tresh && sensorValue2 >= tresh && sensorValue3 >= tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 >= tresh && sensorValue4 >= tresh && sensorValue5 < tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");}

if (sensorValue1 >= tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 >= tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 >= tresh && sensorValue2 >= tresh && sensorValue3 < tresh && sensorValue4 >= tresh && sensorValue5 >= tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 < tresh && sensorValue2 >= tresh && sensorValue3 < tresh && sensorValue4 >= tresh && sensorValue5 < tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 >= tresh && sensorValue2 >= tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 >= tresh)

{  pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 >= tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 >= tresh && sensorValue5 >= tresh)

{ pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

if (sensorValue1 >= tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{ pwm(100,100);

kiri();

lcd.setCursor(0, 1);

lcd.print("kiri");

}

if (sensorValue1 >= tresh && sensorValue2 >= tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{ pwm(100,100);

kiri();

lcd.setCursor(0, 1);

lcd.print("kiri");

}

if (sensorValue1 < tresh && sensorValue2 >= tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{ pwm(100,100);

kiri();

lcd.setCursor(0, 1);

lcd.print("kiri");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 >= tresh)

{ pwm(100,100);

kanan();

lcd.setCursor(0, 1);

lcd.print("kanan");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 >= tresh && sensorValue5 >= tresh)

{ pwm(100,100);

kanan();

lcd.setCursor(0, 1);

lcd.print("kanan");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 >= tresh && sensorValue5 < tresh)

{ pwm(100,100);

kanan();

lcd.setCursor(0, 1);

lcd.print("kanan");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 >= tresh && sensorValue4 >= tresh && sensorValue5 >= tresh)

{ pwm(100,100);

kanan();

lcd.setCursor(0, 1);

lcd.print("kanan");

}

if (sensorValue1 < tresh && sensorValue2 < tresh && sensorValue3 < tresh && sensorValue4 < tresh && sensorValue5 < tresh)

{ pwm(150,150);

maju();

lcd.setCursor(0, 1);

lcd.print("maju");

}

}

//***********************************************//

//****************pwm***************************//

void pwm(byte kiri, byte kanan) {

analogWrite(pwm_ka, kanan);

analogWrite(pwm_ki, kiri);

}

//****************otomatis*********************//

void otomatis() {

sharp = analogRead(sharpPin);

if (sharp >= 350) {

pwm(255,255);

jepit();

delay(1000);

angkat();

kosong();

}

else {

jalan();

sensorValue1 = analogRead(sensorPin1);

sensorValue2 = analogRead(sensorPin2);

sensorValue3 = analogRead(sensorPin3);

sensorValue4 = analogRead(sensorPin4);

sensorValue5 = analogRead(sensorPin5);

if (sensorValue1 >= tresh && sensorValue2 >= tresh && sensorValue3 >= tresh && sensorValue4 >= tresh && sensorValue5 >= tresh)

{

pwm(255,255);

delay(1000);

lepas();

kosong();

}

}

//***********************************************//

//........servo...........//

void awal() {

grip_ka.write(12);

grip_ki.write(180);

grip_te.write(100);

}

void jepit() {

grip_ka.write(108);

grip_ki.write(113);

delay(1000);

grip_te.write(75);

}

void angkat() {

grip_ka.write(12);

grip_ki.write(180);

}

void lepas() {

grip_ka.write(108);

grip_ki.write(113);

delay(1000);

grip_te.write(100);

}

void kosong() {}

//........................................//

void manual() {

pwm(255, 255);

if (error == 1) //skip loop if no controller found

return;

else { //DualShock Controller

ps2x.read_gamepad(false, vibrate); //read controller and set large motor to spin at 'vibrate' speed

if (ps2x.Button(PSB_START))        //will be TRUE as long as button is pressed

{

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("jepit");

grip_te.write(70);

kosong();

}

if (ps2x.Button(PSB_SELECT))

{

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("lepas");

grip_te.write(100);

kosong();

}

if (ps2x.Button(PSB_PAD_UP)) {     //will be TRUE as long as button is pressed

maju();

pwm(100, 100);

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("GO!!!");

}

if (ps2x.Button(PSB_PAD_RIGHT)) {

kanan();

pwm(100, 100);

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("BELOK KANAN");

}

if (ps2x.Button(PSB_PAD_LEFT)) {

kiri();

pwm(100, 100);

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("BELOK KIRI");

}

if (ps2x.Button(PSB_PAD_DOWN)) {

mundur();

pwm(100, 100);

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("MUNDUR");

}

if (ps2x.ButtonPressed(PSB_RED))            //will be TRUE if button was JUST pressed

{

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("angkat");

Serial.println("Circle just pressed");

grip_ka.write(12);

grip_ki.write(180);

kosong();

}

if (ps2x.NewButtonState(PSB_BLUE))           //will be TRUE if button was JUST pressed OR released

{ Serial.println("X just changed");

lcd.clear();

lcd.setCursor(0, 8);

lcd.print("turun");

grip_ka.write(132);

grip_ki.write(115);

kosong();

}

}

delay(50);

}

//.................................//

Tampilan Robot Pembawa Barang

- Tampat atas

(b). Tampak Samping